## Slide 1: MODELLING AND PARAMETRIC PERFORMANCE ANALYSIS OF AN AEM ELECTROLYSER USING ASPEN PLUS
Presented By:
Ankit Saha
Under the guidance of:
Dr. Sourav Mondal
22CH30004
Indian Institute of Technology Kharagpur
Department of Chemical Engineering
1

## Slide 2: ACKNOWLEDGEMENT
Department of Chemical Engineering
2
I am grateful to Prof. Sourav Mondal for his continuous guidance and support during my BTP project.
I sincerely thank Mr. Rajeev Ranjan for helping me at every stage and with every problem during the AWE model preparation in Aspen
I appreciate the support from the department and all who assisted me in completing this work.

## Slide 3: INTRODUCTION
Alkaline Water Electrolyser (AWE)
Mature and low-cost technology
Uses concentrated KOH → corrosion, gas crossover
Limited current densities, diaphragm-based gas separation
Anion Exchange Membrane (AEM) Electrolyser
Operates in alkaline mode but uses a solid polymer membrane
Enables non-precious catalysts, better gas purity, and reduced crossover
Ideal for decentralised, renewable-powered hydrogen systems
Challenges: membrane conductivity, durability, long-term stability
Department of Chemical Engineering
2

## Slide 4: INTRODUCTION
Key Differences
Department of Chemical Engineering
3
Parameter | AWE | AEM
Electrolyte | 20–40 wt% KOH | 0–1 M KOH
Cathode | Ni, Ni–Mo | Ni alloys
Anode | Ni–Co alloys | Ni/Fe/Co oxides
Separator | Diaphragm (~500 µm) | AEM (20–100 µm)
Current Density | 0.2–0.4 A/cm² | 0.2–1.0 A/cm²
Cell Voltage | 1.8–2.4 V | 1.8–2.2 V
Temperature | 60–80 °C | 50–60 °C
H₂ Purity | >99.5% | >99.99%
Technology Status | Mature | Emerging

## Slide 5: OBJECTIVE:
Develop a zero-gap AEM electrolyser model in Aspen Plus using the adapted AWE framework.
Analyse how temperature, current density, and membrane properties affect cell voltage.
Use the AWE-based voltage model to generate performance trends for AEM optimisation.
Department of Chemical Engineering
4

## Slide 6: Model Description
Cathode Half Cell Reaction (HER):
  2H₂O(l) + 2e⁻ ↔ H₂(g) + 2OH⁻(aq) E₀ (298 K) = -0.769 V
Anode Half Cell Reaction (OER):
  2OH⁻(aq) ↔ ½O₂(g) + H₂O(l) + 2e⁻ E₀ (298 K) = +0.460 V
Overall Water Splitting Reaction:
  H₂O(l) ↔ H₂(g) + ½O₂(g) E₀rev (298K)=1.229 V
Department of Chemical Engineering
5
Theory:

## Slide 7: Model Description
The electrochemical equation:-
  Ecell=Erev + act + +
The open circuit equation:-
The reversible cell voltage varies with temperature because it depends on the Gibbs free energy change of the reaction:
The reference paper provides the following standard values:
Substituting these gives a simple expression for the reversible voltage:
Department of Chemical Engineering
6
Theory:

## Slide 8: Activation Overpotential
Activation losses arise from the energy barrier of the electrochemical reactions at both electrodes.
The full Butler–Volmer expression is:
In water electrolysers, the overpotential is large, so one exponential dominates → giving the Tafel approximation.
Department of Chemical Engineering
7
Tafel Form (High Overpotential)
Anode (OER):
Cathode (HER):
Theory:

## Slide 9: Ohmic Overpotential
Ohmic losses mainly arise from OH⁻ transport through the AEM membrane.
Membrane resistance:
Total ohmic drop:
Department of Chemical Engineering
8
Theory:

## Slide 10: Concentration Overpotential
where and are concentrations of Hydrogen and Oxygen, and are concentrations of Hydrogen and Oxygen at standard conditions, m|e is membrane and electrode interface
Department of Chemical Engineering
9
Theory:

## Slide 11: Aspen Semi-Empirical Voltage Model
The AEM electrolyser voltage in Aspen Plus is represented using a semi-empirical relation:
𝑉=𝐸rev+𝑟𝐼+𝑠ln⁡(1+𝑡𝐼)
Term meanings:
  : reversible thermodynamic voltage
  : linear ohmic contribution
  𝑠ln⁡(1+𝑡𝐼) : combined activation + concentration overpotential
Model notes:
  Aspen provides the parameters , , and .
  The logarithmic term inherently captures Tafel-type behaviour, suitable for both AWE and AEM technology.
  Therefore, no additional parameter tuning was necessary for this work.
Department of Chemical Engineering
10
Methodology:

## Slide 12: Aspen Semi-Empirical Voltage Model
Department of Chemical Engineering
11
Methodology:
Parameter | Value
Cathode Active Area | 1 cm²
Anode Active Area | 1 cm²
Thickness of cathode electrode | 250 µm
Thickness of anode electrode | 250 µm
Membrane Active Area | 9 cm²
Membrane Thickness | 60 µm
Stacks | 1
Cells per stack | 1
Reference anode exchange current density | 0.001
Reference cathode exchange current density | 1×10⁻⁵
Structure Parameter
Parameter | Value
Total current | 0.6 A
Temperature of electrolyser | 20 °C
Feed flow rate | 1.56 mL/min
Concentration of KOH | 0.1 M
Feed-to-anode ratio | 0.5
Operational Parameter

## Slide 13: Outlet flow and composition:-
Department of Chemical Engineering
12
Result and Discussion:
Hydrogen (CAT-OUT):
Vapor molar flow: 1.106×10⁻⁵ kmol h⁻¹
Vapor mole fraction (gas purity basis): 0.9767 ≈ 97.7 % H₂
Oxygen (AN-OUT):
Vapor molar flow: 5.506×10⁻⁶ kmol h⁻¹
Vapor mole fraction (gas purity basis): 0.9688 ≈ 96.9 % O₂
Voltage and efficiencies:
Cell voltage: 1.984 V at 0.6 A
Voltage efficiency (Total): 0.747
Overpotential breakdown:
Activation (total): 0.512 V (anode 0.198 V, cathode 0.313 V).
Ohmic: 0.239 V.
Concentration: 1.45×10⁻⁴ V (negligible).

## Slide 14: Polarization Curve:
The model matches the experimental polarization curve well, capturing both the activation region at low currents and the linear ohmic region at higher currents, with only minor deviations at very low currents.
Department of Chemical Engineering
13
Result and Discussion:

## Slide 15: Overpotential Distribution:
Overpotential Distribution
Activation overpotentials at both electrodes rise sharply at low current densities due to slower reaction kinetics, with the cathode showing higher losses because hydrogen evolution is less favorable and requires a larger driving force.
Ohmic overpotential increases almost linearly with current density as membrane and electrolyte resistance dominate.
Overall, the cell is activation-controlled at low currents and becomes ohmic-controlled at higher currents.
Department of Chemical Engineering
14
Result and Discussion:

## Slide 16: H2 production and voltage efficiency
Efficiency–Production Trade-off
The hydrogen production and voltage efficiency curves intersect at ~0.52 A/cm², where the voltage efficiency is ~77% (cell voltage ≈ 1.87 V).
At this point, the hydrogen production rate is ~12 mL/day, representing a balanced operating “sweet spot.”
Beyond this current density, hydrogen output increases further, but voltage efficiency decreases noticeably.
Department of Chemical Engineering
15
Result and Discussion:

## Slide 17: Effect of KOH concentration
Effect of Electrolyte Concentration
Increasing KOH concentration from 0.01 M → 0.1 M → 1 M reduces the cell voltage at a given current density.
Higher concentration provides more OH⁻ ions, improving ionic conductivity and lowering ohmic resistance.
At 0.01 M, limited OH⁻ availability causes poor ionic transport and higher activation losses, leading to a steep voltage rise even at low currents.
1 M KOH gives the lowest voltage due to better ion mobility and stable reaction conditions.
Overall, higher electrolyte concentration improves cell performance by reducing resistive losses.
Department of Chemical Engineering
16
Result and Discussion:

## Slide 18: Effect of electrolyser temperature
Department of Chemical Engineering
17
Result and Discussion:
Cell voltage decreases as temperature increases due to faster reaction kinetics and higher ionic conductivity.
Both activation and ohmic losses are reduced at elevated temperatures, lowering the voltage at the same current density.
The improvement from 20°C → 40°C is significant, while 40°C → 60°C shows a smoother but still clear reduction.

## Slide 19: Effect of membrane thickness
Department of Chemical Engineering
18
Result and Discussion:
Cell voltage increases with membrane thickness because a thicker AEM adds more ionic transport resistance.
OH⁻ ions must travel a longer distance, increasing the ohmic overpotential.
The 90 μm membrane shows the highest voltages, while the 30 μm membrane performs best across all currents.
Differences between curves become larger at high current densities where ohmic losses dominate.

## Slide 20: Effect of feed flow rate:
Department of Chemical Engineering
19
Result and Discussion:
Polarization curves for 1.56, 3.12, and 4.68 mL/min nearly overlap, showing only a minor voltage drop at higher flow rates.
This indicates that flow rate has no significant impact on cell voltage in this range.
In a zero-gap electrolyser, water supply is governed mainly by membrane hydration and reaction consumption, so increasing bulk flow does not noticeably change local reaction conditions.

## Slide 21: Conclusion:
Department of Chemical Engineering
20
A zero-gap AEM electrolyser model was developed in Aspen Plus using the adapted AWE electrochemical framework.
The model closely matched the experimental polarization curve, confirming its validity.
Higher temperatures improved performance by reducing activation and ohmic losses.
Increasing electrolyte concentration lowered cell voltage by enhancing OH⁻ conductivity.
Thinner membranes reduced ohmic resistance and improved efficiency.
Exchange current densities affected activation losses, with the anode showing stronger sensitivity.
Feed flow rate had negligible impact on voltage or hydrogen production.

## Slide 22: Future Work:
Department of Chemical Engineering
21
Extend the single-cell model to a stack-level simulation to study scalability, voltage balancing, heat distribution, membrane hydration, and gas crossover in larger systems.
Perform a detailed energy and process analysis in Aspen to identify required utilities (heaters, coolers, pumps, separators) and evaluate overall energy demand and heat-integration potential.
Assess KOH recyclability by modelling a closed-loop electrolyte recovery system to reduce chemical consumption and improve sustainability.

## Slide 23: References:
Department of Chemical Engineering
22
1. Lawand, K., Nuggehalli Sampathkumar, S., Mury, Z., & Van Herle, J. (2024). Membrane electrode assembly simulation of anion exchange membrane water electrolysis. Journal of Power Sources, 595, 234047.
2. Gunuru, M., & Paravada, M. (2025). Mathematical modelling of an AEMWE: Investigating optimum operating conditions of an alkaline-fed AEM electrolyser. International Journal of Hydrogen Energy, 50, 332550
3. An, L., Zhao, T. S. Chai, Z. H. Tan, P., & Zeng L. (2014). Mathematical modeling of an anion-exchange membrane water electrolyzer for hydrogen production. International Journal of Hydrogen Energy, 39(35), 19869–19876.
4. H. A. Miller , Bouzek K., Hnat, J., Loos, S., Bernäcker, C. I., Weißgärber, T., Röntzsch, L., & Meier-Haack, J. (2020). Green hydrogen from anion exchange membrane water electrolysis: A review of recent developments in critical materials and operating conditions. Sustainable Energy & Fuels, 4, 2114–2133.
5. Du, N., Roy, C., Peach, R., Turnbull, M., Thiele, S., & Bock, C. (2022). Anion-exchange membrane water electrolyzers. Chemical Reviews, 122(14), 11830–11895
.6. Ulleberg, Ø. (2003). Modeling of advanced alkaline electrolyzers: A system simulation approach. International Journal of Hydrogen Energy, 28(1–2), 21–33.
7. Aspen documentation on AWE electrolyzers.
8. Du, N., Roy, C., Peach, R., Turnbull, M., Thiele, S., & Bock, C. (2022). Anion-exchange membrane water electrolyzers. Chemical Reviews, 122(14), 11830–11895.